## Slide 1
UNIT-III
MAC PROTOCOLS FOR WIRELESS SENSOR NETWORKS
Contents:
Issues in Designing a MAC protocol for Ad-hoc Wireless Networks
Design goals of a MAC Protocol for Ad-hoc Wireless Networks
Classifications of MAC Protocols
Contention-Based Protocols
Contention-Based Protocols with reservation Mechanisms
Contention-Based MAC Protocols with Scheduling Mechanisms
MAC Protocols that use Directional Antennas, Other MAC

## Slide 2
INTRODUCTION TO MAC:
Nodes in an Ad-hoc wireless network share a common broadcast radio channel. Since the radio spectrum is limited, the bandwidth available for communication in such networks is also limited.
Access to this shared medium should be controlled in such a manner that all nodes receive a fair share of the available bandwidth, and that the bandwidth is utilized efficiently.
Characteristics of the wireless medium are completely different from wired medium.
So a different set of protocols is required for controlling access to the shared medium in such networks. This is achieved by using Medium Access Control (MAC) protocol.
Click to add text

## Slide 3
Issues in Designing MAC Protocol for Ad-hoc
Wireless Networks:
Bandwidth Efficiency:
Since the radio spectrum is limited, the bandwidth available for communication is also very limited. The MAC protocol must be designed in such a way that to maximize this bandwidth efficiency (the ratio of the bandwidth used for actual data transmission to the total available bandwidth).
That is the uncommon bandwidth is utilized in an efficient manner.
Quality of Service Support(QoS):
Providing QoS support to data sessions in Ad-hoc networks is very difficult due to their characteristic nature of nodes mobility.
Most of the time, Bandwidth reservation made at one point of time may become invalid once the node moves out of the region.
The MAC protocol for Ad-hoc wireless networks that are to be used in such real-time applications must have resource reservation mechanism take care of nature of the wireless channel and the mobility of nodes.

## Slide 4
Issues in Designing MAC Protocol for Ad-hoc
Wireless Networks:
Synchronization:
The MAC protocol must take into consideration the synchronization between nodes in the network.
Synchronization is very important for bandwidth (time slot) reservations by nodes achieved by exchange of control packets.
Hidden and Exposed Terminal Problems:
The hidden terminal problem refers to the collision of packets at a receiving node due to the simultaneous transmission of those nodes.
The exposed terminal problem refers to the inability of a node, which is blocked due to transmission by a nearby transmitting node, to transmit to another node.
Mobility of Nodes:
This is a very important factor affecting the performance (throughput) of the protocol.
The MAC protocol obviously has no role to play in influencing the mobility of the nodes.

## Slide 5
Issues in Designing MAC Protocol for Ad-hoc
Wireless Networks:
Error-Prone Shared Broadcast Channel:
Due to broadcast nature of the radio channel (transmissions made by a node are received by all nodes within its direct transmission range) there is a possibility of packet collisions is quite high in wireless networks.
A MAC protocol should grant channel access to nodes in such a manner that collisions are minimized.
Distributed Nature/Lack of Central Coordination
Ad hoc wireless networks do not have centralized coordinators because nodes keep moving continuously.
Therefore, nodes must be scheduled in a distributed fashion for gaining access to the channel.
The MAC protocol must make sure that the additional overhead, in terms of bandwidth consumption is not very high.

## Slide 6
Design goals of a MAC Protocol for Ad-hoc Wireless Networks:
The operation of the protocol should be distributed.
The protocol should provide QoS support for real-time traffic.
The access delay, which refers to the average delay experienced by any packet to get transmitted, must be kept low.
The available bandwidth must be utilized efficiently.
The protocol should ensure fair allocation of bandwidth to nodes.
Control overhead must be kept as low as possible.
The protocol should minimize the effects of hidden and exposed terminal problems.
The protocol must be scalable to large networks.
It should have power control mechanisms.
The protocol should have mechanisms for adaptive data rate control.
It should try to use directional antennas.
The protocol should provide synchronization among nodes.

## Slide 7
Classifications of MAC Protocols:
Ad hoc network MAC protocols can be classified into three types:
    Contention-based protocols
    Contention-based protocols with reservation mechanisms
    Contention-based protocols with scheduling mechanisms
    Other MAC protocols

## Slide 8
Classifications of MAC Protocols:
Contention-based protocols:
  Sender-initiated protocols: Packet transmissions are initiated by the sender node.
    Single-channel sender-initiated protocols: A node that wins the contention to the channel can make use of the entire bandwidth.
    Multichannel sender-initiated protocols: The available bandwidth is divided into multiple channels.
  Receiver-initiated protocols: The receiver node initiates the contention resolution protocol.
Contention-based protocols with reservation mechanisms
  Synchronous protocols: All nodes need to be synchronized. Global time synchronization is difficult to achieve.
  Asynchronous protocols: These protocols use relative time information for effecting reservations.

## Slide 9
Classifications of MAC Protocols:
Contention-based protocols with scheduling mechanisms:
  Node scheduling is done in a manner so that all nodes are treated fairly and no node is starved of bandwidth.
  Scheduling-based schemes are also used for enforcing priorities among flows whose packets are queued at nodes.
  Some scheduling schemes also consider battery characteristics.
Other protocols are those MAC protocols : These are not strictly fall under the above categories.

## Slide 10
Classifications of MAC Protocols:
Contention-based protocols :
Single-channel sender-initiated protocols:
EXAMPLES: MACAW, FAMA
MACAW: A Media Access Protocol for Wireless LANs is based on MACA (Multiple Access Collision Avoidance) Protocol
MACA:-
  When a node wants to transmit a data packet, it first transmit a RTS (Request To Send) frame.
  The receiver node, on receiving the RTS packet, if it is ready to receive the data packet, transmits a CTS (Clear to Send) packet.
  Once the sender receives the CTS packet without any error, it starts transmitting the data packet.
  If a packet transmitted by a node is lost, the node uses the Binary Exponential Back-off (BEB) algorithm to back-off a random interval of time before retrying. The problem is solved by MACAW

## Slide 11
Classifications of MAC Protocols:
Contention-based protocols : …cntd
Single-channel sender-initiated protocols:
MACA EXAMPLES:
MACA avoids the problem of hidden terminals
  A and C want to send to B
  A sends RTS first
  C waits after receiving
  CTS from B
MACA avoids the problem of exposed terminals
  B wants to send to A, C to another terminal
  now C does not have to wait for it cannot receive CTS from A

## Slide 12
Classifications of MAC Protocols:
Contention-based protocols : …cntd
Single-channel sender-initiated protocols:
MACAW: (MACA for Wireless) is a revision of MACA.
  The sender transmits a RTS (Request To Send) frame if no nearby station transmits a RTS.
  The receiver replies with a CTS (Clear To Send) frame.
  Neighbors
      see CTS, then keep quiet.
      see RTS but not CTS, then keep quiet until the CTS is back to the sender.
  The receiver sends an ACK when receiving an frame.
      Neighbors keep silent until see ACK.
  Collisions
      There is no collision detection.
      The senders know collision when they don’t receive CTS.
      They each wait for the exponential back-off time.

## Slide 13
Classifications of MAC Protocols:
Contention-based protocols : …cntd
Single-channel sender-initiated protocols:
FAMA: Floor Acquisition Multiple Access Protocols.
Channel access consists of a carrier-sensing operation and a collision avoidance
Carrier-sensing by the sender, followed by the RTS-CTS control packet exchange.
  Data transmission to be collision free, the duration of an RTS must be at least twice the maximum channel propagation delay
Two FAMA protocol variants
  RTS-CTS exchange with no carrier sensing (MACA)
  RTS-CTS exchange with non-persistent carrier sensing (FAMA-NTR)
  FAMA-NTR(Non-persistent Transmit Request)
Before sending a packet, the sender senses the channel
If channel is busy, the sender back-off a random time and retries later
If the channel is free, the sender sends RTS and waits for a CTS packet
If the sender cannot receive a CTS, it takes a random back-off and retries later
If the sender receives a CTS, it can start transmission data packet
In order to allow the sender to send a burst of packets, the receiver is made to wait a time duration τ seconds after a packet is received.

## Slide 14
Classifications of MAC Protocols:
Contention-based protocols : …cntd
Multi-channel sender-initiated protocols:
Busy Tone Multiple Access Protocols (BTMA):
  The transmission channel is split into two parts:
      a data channel for data packet transmissions
      a control channel used to transmit the busy tone signal
  When a node is ready for transmission, it senses the channel to check whether the busy tone is active.
    If not, it turns on the busy tone signal and starts data transmissions.
    Otherwise, it reschedules the packet for transmission after some random rescheduling delay.
Dual Busy Tone Multiple Access Protocol (DBTMAP) is an extension of the BTMA scheme.
    a data channel for data packet transmissions
    a control channel used for control packet transmissions (RTS and CTS packets) and also for transmitting the busy tones.
    Use two busy tones on the control channel, BTt and BTr.
      BTt : indicate that it is transmitting on the data channel
      BTr: indicate that it is receiving on the data channel
    Two busy tone signals are two sine waves at different frequencies

## Slide 15
Classifications of MAC Protocols:
Contention-based protocols : …cntd
Receiver-initiated protocols:
RI-BTMA: Receiver-Initiated Busy Tone Multiple Access Protocol
  The transmission channel is split into two:
    a data channel for data packet transmissions
    a control channel used for transmitting the busy tone signal
  A node can transmit on the data channel only if it finds the busy tone to be absent on the control channel.
  The data packet is divided into two portions: a preamble and the actual data packet.
MACA-BI: MACA-By Invitation
  By eliminating the need for the RTS packet it reduces the number of control packets used in the MACA protocol which uses the three-way handshake mechanism.
MARCH: Media Access with Reduced Handshake.

## Slide 16
Classifications of MAC Protocols:
Contention-based protocols : …cntd
Receiver-initiated protocols:

## Slide 17
Classifications of MAC Protocols:
Contention-based Protocols with Reservation Mechanism:
  Contention occurs during the resource (bandwidth) reservation phase.
  Once the bandwidth is reserved, the node gets exclusive access to the reserved bandwidth.
  QoS support can be provided for real-time traffic.
  Synchronous protocols:
  Distributed Packet Reservation Multiple Access Protocol(D-PRMA)
    It extends the centralized packet reservation multiple access (PRMA) scheme into a distributed scheme that can be used in ad hoc wireless networks.
    PRMA was designed in a wireless LAN with a base station.
    D-PRMA is a TDMA-based scheme. The channel is divided into fixed- and equal-sized frames along the time axis.

## Slide 18
Classifications of MAC Protocols: …cntd
Contention-based Protocols with Reservation Mechanism:
  Synchronous protocols:
  Collision Avoidance Time Allocation Protocol(CATA):
Support broadcast, unicast, and multicast transmissions simultaneously.
Each frame consists of S slots and each slot is further divided into five Control Mini-Slots
    CMS1: Slot Reservation (SR)
    CMS2: RTS
    CMS3: CTS
    CMS4: Not To Send (NTS)
    DMS: Data transmission

## Slide 19
Classifications of MAC Protocols: …cntd
Contention-based Protocols with Reservation Mechanism:
  Synchronous protocols:
  Hop Reservation Multiple Access Protocol (HRMA):
    A multichannel MAC protocol which is based on half-duplex, very slow frequency-hopping spread spectrum (FHSS) radios
    Uses a reservation and handshake mechanism to enable a pair of communicating nodes to reserve a frequency hop, thereby guaranteeing collision-free data transmission.
    Can be viewed as a time slot reservation protocol where each time slot is assigned a separate frequency channel.

## Slide 20
Classifications of MAC Protocols: …cntd
Contention-based Protocols with Reservation Mechanism:
  Synchronous protocols:
  Soft Reservation Multiple Access with Priority Assignment (SRMA/PA):
    Developed with the main objective of supporting integrated services of real-time and non-real-time application in Ad-hoc networks.
    Nodes use a collision-avoidance handshake mechanism and a soft reservation mechanism.
  Five-Phase Reservation Protocol (FPRP)
    A single-channel TDMA based broadcast scheduling protocol.
    Nodes uses a contention mechanism in order to acquire time slots.
    The protocol assumes the availability of global time at all nodes.
    The reservation takes five phases:
      Reservation,
      Collision Report,
      Reservation Confirmation,
      Reservation Acknowledgement,
      Packing And Elimination Phase.

## Slide 21
Classifications of MAC Protocols: …cntd
Contention-based Protocols with Reservation Mechanism:
  Synchronous protocols:
  Five-Phase Reservation Protocol (FPRP)
Five-phase protocol:
Reservation request: send reservation request (RR) packet to dest.
Collision report: if a collision is detected by any node, that node broadcasts a CR packet
Reservation confirmation: a source node won the contention will send a RC packet to destination node if it does not receive any CR message in the previous phase
Reservation acknowledgment: destination node acknowledge reception of RC by sending back RA message to source
Packing and elimination: use packing packet and elimination packet.

## Slide 22
Classifications of MAC Protocols: …cntd
Contention-based Protocols with Reservation Mechanism:
  Asynchronous protocols:
MACA with Piggy-Backed Reservation (MACA/PR):
  Provide real-time traffic support in multi-hop wireless networks
  Based on the MACAW protocol with non-persistent CSMA
  The main components of MACA/PR are:
      A MAC protocol
      A reservation protocol
      A QoS routing protocol
Real-Time Medium Access Control Protocol (RTMAC)
  Provides a bandwidth reservation mechanism for supporting real-time traffic in ad-hoc wireless networks
  RTMAC has two components
    A MAC layer protocol is a real-time extension of the IEEE 802.11 DCF.
        A medium-access protocol for best-effort traffic
        A reservation protocol for real-time traffic
    A QoS routing protocol is responsible for end-to-end reservation and release of bandwidth resources.

## Slide 23
Classifications of MAC Protocols:
Contention-based protocols with Scheduling Mechanism:
Protocols in this category focus on packet scheduling at the nodes and transmission scheduling of the nodes.
The factors that affects scheduling decisions
  Delay targets of packets
  Traffic load at nodes
  Battery power
Distributed priority scheduling and medium access in Ad Hoc Networks present two mechanisms for providing quality of service (QoS)
  Distributed priority scheduling (DPS) – Piggy-backs the priority tag of a node’s current and head-of-line packets to the control and data packets
  Multi-hop coordination – Extends the DPS scheme to carry out scheduling over multi-hop paths.

## Slide 24
Classifications of MAC Protocols: …cntd
Contention-based protocols with Scheduling Mechanism:
Distributed Wireless Ordering Protocol (DWOP)
  A media access scheme along with a scheduling mechanism based on the distributed priority scheduling scheme
Distributed Laxity-based Priority Scheduling (DLPS) Scheme
  Scheduling decisions are made based on the states of neighboring nodes and feed back from destination nodes regarding packet losses
  Packets are recorded based on their uniform laxity budgets (ULBs) and the packet delivery ratios of the flows. The laxity of a packet is the time remaining before its deadline.

## Slide 25
Classifications of MAC Protocols:
MAC Protocols that use directional Antennas:
MAC protocols that use directional antennas have several advantages:
  Reduce signal interference
  Increase in the system throughput
  Improved channel reuse
MAC protocol using directional antennas
  Make use of an RTS/CTS exchange mechanism
  Use directional antennas for transmitting and receiving data packets
Directional Busy Tone-based MAC Protocol (D-BTMA)
  It uses directional antennas for transmitting the RTS, CTS, data frames, and the busy tones.
Directional MAC Protocols for Ad Hoc Wireless Networks
  DMAC-1: A directional antenna is used for transmitting RTS packets and Omni-directional antenna for CTS packets.
  DMAC-1, both directional RTS and omni-directional RTS transmission are used.

## Slide 26
Classifications of MAC Protocols: …cntd
MAC Protocols that use directional Antennas:

## Slide 27
Classifications of MAC Protocols: …cntd
Other MAC Protocols:
Multi-channel MAC Protocol (MMAC)
  Multiple channels for data transmission
  There is no dedicated control channel.
  Based on channel usage channels can be classified into three types: high, medium and low preference channels.
Multi-channel Carrier Sense Multiple Access(MCSMA) MAC Protocol :
  The available bandwidth is divided into several channels
Power Control MAC Protocol (PCM) for Ad Hoc Networks
  Allows nodes to vary their transmission power levels on a per-packet basis
Receiver-based Autorate Protocol (RBAR)
  Use a rate adaptation approach
Interleaved Carrier-Sense Multiple Access Protocol (ICSMA)
  The available bandwidth is split into tow equal channels
  The handshaking process is interleaved between the two channels.

## Slide 28
Note: A directional antenna or beam antenna is an antenna which radiates or receives greater power in specific directions allowing for increased performance and reduced interference from unwanted sources.
Note: Omnidirectional refers to the notion(feeling) of existing in every direction. Omnidirectional antenna is that radiates equally in all directions.
Note: Handshaking is the exchange of information between two modems and the resulting agreement about which protocol to use that precedes each telephone connection.