## Slide 1: PART-A SECURITY IN AD HOC WIRELESS NETWORKS
Security in Ad Hoc Wireless Networks
Network Security Requirements
Issues and Challenges in Security
Provisioning
Network Security Attacks
Key Management
Secure Routing in Ad Hoc Wireless Networks
Click to add text

## Slide 2: INTRODUCTION
Due to the unique characteristics of ad hoc wireless networks, such networks are highly vulnerable to security attacks compared to wired networks or infrastructure-based wireless networks

## Slide 3: NETWORK SECURITY REQUIREMENTS
Confidentiality: The data sent by the sender (source node) must be comprehensible only to the intended receiver (destination node). Though an intruder might get hold of the data being sent, he/she must not be able to derive any useful information out of the data. One of the popular techniques used for ensuring confidentiality is data encryption.

## Slide 4: Contd..
Integrity: The data sent by the source node should reach the destination node as it was sent: unaltered. In other words, it should not be possible for any malicious node in the network to tamper with the data during transmission.
Availability: The network should remain operational all the time. It must be robust enough to tolerate link failures and also be capable of surviving various attacks mounted on it. It should be able to provide the guaranteed services whenever an authorized user requires them.
Non-repudiation: Non-repudiation is a mechanism to guarantee that the sender of a message cannot later deny having sent the message and that the recipient cannot deny having received the message. Digital signatures, which function as unique identifiers for each user, much like a written signature, are used commonly for this purpose.

## Slide 5: ISSUES AND CHALLENGES IN SECURITY PROVISIONING
• Shared broadcast radio channel: Unlike in wired networks where a separate dedicated transmission line can be provided between a pair of end users, the radio channel used for communication in ad hoc wireless networks is broadcast in nature and is shared by all nodes in the network. Data transmitted by a node is received by all nodes within its direct transmission range. So a malicious node could easily obtain data being transmitted in the network. This problem can be minimized to a certain extent by using directional antennas.
• Insecure operational environment: The operating environments where ad hoc wireless networks are used may not always be secure. One important application of such networks is in battlefields. In such applications, nodes may move in and out of hostile and insecure enemy territory, where they would be highly vulnerable to security attacks.

## Slide 6: Contd..
• Lack of central authority: In wired networks and infrastructure-based wireless networks, it would be possible to monitor the traffic on the network through certain important central points (such as routers, base stations, and access points) and implement security mechanisms at such points. Since ad hoc wireless networks do not have any such central points, these mechanisms cannot be applied in ad hoc wireless networks.
Lack of association: Since these networks are dynamic in nature, a node can join or leave the network at any point of the time. If no proper authentication mechanism is used for associating nodes with a network, an intruder would be able to join into the network quite easily and carry out his/her attacks.

## Slide 7: Contd..
Limited resource availability: Resources such as bandwidth, battery power, and computational power (to a certain extent) are scarce in ad hoc wireless networks. Hence, it is difficult to implement complex cryptography-based security mechanisms in such networks.
Physical vulnerability: Nodes in these networks are usually compact and hand-held in nature. They could get damaged easily and are also vulnerable to theft.

## Slide 8: NETWORK SECURITY ATTACKS

## Slide 9: Network Layer Attacks
Wormhole attack: In this attack, an attacker receives packets at one location in the network and tunnels them (possibly selectively) to another location in the network, where the packets are resent into the network.
This tunnel between two colluding attackers is referred to as a wormhole. It could be established through a single long-range wireless link or even through a wired link between the two colluding attackers.

## Slide 10: Contd..
Due to the broadcast nature of the radio channel, the attacker can create a wormhole even for packets not addressed to itself.
Though no harm is done if the wormhole is used properly for efficient relaying of packets, it puts the attacker in a powerful position compared to other nodes in the network, which the attacker could use in a manner that could compromise the security of the network.
If proper mechanisms are not employed to defend the network against wormhole attacks, most of the existing routing protocols for ad hoc wireless networks may fail to find valid routes.

## Slide 11: Contd..
Blackhole attack: In this attack, a malicious node falsely advertises good paths (e.g., shortest path or most stable path) to the destination node during the path-finding process (in on-demand routing protocols) or in the route update messages (in table-driven routing protocols).
The intention of the malicious node could be to hinder the path-finding process or to intercept all data packets being sent to the destination node concerned.

## Slide 12: Contd..
Byzantine attack: Here, a compromised intermediate node or a set of compromised intermediate nodes works in collusion and carries out attacks such as creating routing loops, routing packets on non-optimal paths, and selectively dropping packets.
Byzantine failures are hard to detect.
The network would seem to be operating normally in the viewpoint of the nodes, though it may actually be exhibiting Byzantine behavior

## Slide 13: Contd..
Information disclosure: A compromised node may leak confidential or important information to unauthorized nodes in the network. Such information may include information regarding the network topology, geographic location of nodes, or optimal routes to authorized nodes in the network.

## Slide 14: Contd..
Resource consumption attack: In this attack, a malicious node tries to consume/waste away resources of other nodes present in the network.
The resources that are targeted are battery power, bandwidth, and computational power, which are only limitedly available in ad hoc wireless networks.
The attacks could be in the form of unnecessary requests for routes, very frequent generation of beacon packets, or forwarding of stale packets to nodes.
Using up the battery power of another node by keeping that node always busy by continuously pumping packets to that node is known as a sleep deprivation attack.

## Slide 15: Contd..
Routing attacks: There are several types attacks mounted on the routing protocol which are aimed at disrupting the operation of the network. In what follows, the various attacks on the routing protocol are described briefly
– Routing table overflow: In this type of attack, an adversary node advertises routes to non-existent nodes, to the authorized nodes present in the network. The main objective of such an attack is to cause an overflow of the routing tables, which would in turn prevent the creation of entries corresponding to new routes to authorized nodes. Proactive routing protocols are more vulnerable to this attack compared to reactive routing protocols.
– Routing table poisoning: Here, the compromised nodes in the networks send fictitious routing updates or modify genuine route update packets sent to other uncompromised nodes. Routing table poisoning may result in sub-optimal routing, congestion in portions of the network, or even make some parts of the network inaccessible.

## Slide 16: Contd..
– Packet replication: In this attack, an adversary node replicates stale packets. This consumes additional bandwidth and battery power resources available to the nodes and also causes unnecessary confusion in the routing process.
– Route cache poisoning: In the case of on-demand routing protocols each node maintains a route cache which holds information regarding routes that have become known to the node in the recent past. Similar to routing table poisoning, an adversary can also poison the route cache to achieve similar objectives.
– Rushing attack: On-demand routing protocols that use duplicate suppression during the route discovery process are vulnerable to this attack. An adversary node which receives a RouteRequest packet from the source node floods the packet quickly throughout the network before other nodes which also receive the same RouteRequest packet can react.

## Slide 17: Transport Layer Attacks
• Session hijacking: Here, an adversary takes control over a session between two nodes. Since most authentication processes are carried out only at the start of a session, once the session between two nodes gets established, the adversary node masquerades as one of the end nodes of the session and hijacks the session.

## Slide 18
Application Layer Attacks
Repudiation: In simple terms, repudiation refers to the denial or attempted denial by a node involved in a communication of having participated in all or part of the communication. As mentioned non-repudiation is one of the important requirements for a security protocol in any communication network.

## Slide 19: Other Attacks
Multi-layer Attacks
Multi-layer attacks are those that could occur in any layer of the network protocol stack. Denial of service and impersonation are some of the common multi-layer attacks. This section discusses some of the multi-layer attacks in ad hoc wireless networks.
• Denial of Service: In this type of attack, an adversary attempts to prevent legitimate and authorized users of services offered by the network from accessing those services. A denial of service (DoS) attack can be carried out in many ways. The classic way is to flood packets to any centralized resource (e.g., an access point) used in the network so that the resource is no longer available to nodes in the network, resulting in the network no longer operating in the manner it was designed to operate.
This may lead to a failure in the delivery of guaranteed services to the end users.

## Slide 20
– Jamming: In this form of attack, the adversary initially keeps monitoring the wireless medium in order to determine the frequency at which the receiver node is receiving signals from the sender. It then transmits signals on that frequency so that error-free reception at the receiver is hindered. Frequency hopping spread spectrum (FHSS) and direct sequence spread spectrum (DSSS) (described in detail in the first chapter of this book) are two commonly used techniques that overcome jamming attacks.
– SYN flooding: Here, an adversary sends a large number of SYN packets8 to a victim node, spoofing the return addresses of the SYN packets. On receiving the SYN packets, the victim node sends back acknowledgment (SYN-ACK) packets to nodes whose addresses have been specified in the received SYN packets.
– Distributed DoS attack: A more severe form of the DoS attack is the distributed DoS (DDoS) attack. In this attack, several adversaries that are distributed throughout the network collude and prevent legitimate users from accessing the services offered by the network.

## Slide 21
• Impersonation: In impersonation attacks, an adversary assumes the identity and privileges of an authorized node, either to make use of network resources that may not be available to it under normal circumstances, or to disrupt the normal functioning of the network by injecting false routing information into the network. An adversary node could masquerade as an authorized node using several methods. It could by chance guess the identity and authentication details of the authorized node (target node), or it could snoop for information regarding the identity and authentication of the target node from a previous communication, or it could circumvent or disable the authentication mechanism at the target node.
Device Tampering
Unlike nodes in a wired network, nodes in ad hoc wireless networks are usually compact, soft, and hand-held in nature. They could get damaged or stolen easily

## Slide 22: KEY MANAGEMENT
Cryptography is one of the most common and reliable means to ensure security.
Cryptography is not specific to ad hoc wireless networks. It can be applied to any communication network.
It is the study of the principles, techniques, and algorithms by which information is transformed into a disguised version which no unauthorized person can read, but which can be recovered in its original form by an intended recipient.

## Slide 23: Contd..
In the parlance of cryptography, the original information to be sent from one person to another is called plaintext.
This plaintext is converted into ciphertext by the process of encryption, that is, the application of certain algorithms or functions.
An authentic receiver can decrypt/decode the ciphertext back into plaintext by the process of decryption.
The processes of encryption and decryption are governed by keys, which are small amounts of information used by the cryptographic algorithms.
When the key is to be kept secret to ensure the security of the system, it is called a secret key.
The secure administration of cryptographic keys is called key management.

## Slide 24: Cntd..
The four main goals of cryptography are confidentiality, integrity, authentication (the receiver should be able to identify the sender and verify that the message actually came from that sender), and non-repudiation
There are two major kinds of cryptographic algorithms: symmetric key algorithms, which use the same key for encryption and decryption, and asymmetric key algorithms, which use two different keys for encryption and decryption

## Slide 25
Symmetric key algorithms are usually faster to execute electronically, but require a secret key to be shared between the sender and receiver.
When communication needs to be established among a group of nodes, each sender-receiver pair should share a key, which makes the system non-scalable. If the same key is used among more than two parties, a breach of security at any one point makes the whole system vulnerable.

## Slide 26
The asymmetric key algorithms are based on some mathematical principles which make it infeasible or impossible to obtain one key from another; therefore, one of the keys can be made public while the other is kept secret (private). This is called public key cryptography.
Such systems are used extensively in practice, but are not provably secure. They rely upon the difficulty of solving certain mathematical problems, and the network would be open to attacks once the underlying mathematical problem is solved.

## Slide 27: Symmetric Key Algorithms
Symmetric key algorithms rely on the presence of the shared key at both the sender and receiver, which has been exchanged by some previous arrangement.
There are two kinds of symmetric key algorithms, one involving block ciphers and the other stream ciphers. A block cipher is an encryption scheme in which the plaintext is broken into fixed-length segments called blocks, and the blocks are encrypted one at a time.
The simplest examples include substitution and transposition. In substitution, each alphabet of the plaintext is substituted by another in the cipher text, and this table mapping the original and the substituted alphabet is available at both the sender and receiver

## Slide 29
A stream cipher is, in effect, a block cipher of block length one.
One of the simplest stream ciphers is the Vernam cipher, which uses a key of the same length as the plaintext for encryption.
For example, if the plaintext is the binary string 10010100, and the key is 01011001, then the encrypted string is given by the XOR of the plaintext and key, to be 11001101.
The plaintext is again recovered by XORing the cipher text with the same key. If the key is randomly chosen, transported securely to the receiver, and used for only one communication, this forms the one-time pad which has proven to be the most secure of all cryptographic systems.
The only bottleneck here is to be able to securely send the key to the receiver.

## Slide 30: Asymmetric Key Algorithms
Asymmetric key (or public key) algorithms use different keys at the sender and receiver ends for encryption and decryption, respectively.
Let the encryption process be represented by a function E, and decryption by D. Then the plaintext m is transformed into the ciphertext c as c = E(m).
The receiver then decodes c by applying D. Hence, D is such that m = D(c) = D(E(m)). When this asymmetric key concept is used in public key algorithms, the key E is made public, while D is private, known only to the intended receiver.
Anyone who wishes to send a message to this receiver encrypts it using E. Though c can be overheard by adversaries, the function E is based on a computationally difficult mathematical problem, such as the factorization of large prime numbers.
Hence, it is not possible for adversaries to derive D given E. Only the receiver can decrypt c using the private key D.

## Slide 31: Key Management Approaches
The primary goal of key management is to share a secret (some information) among a specified set of participants
There are several methods that can be employed to perform this operation, all of them requiring varying amounts of initial configuration, communication, and computation.
The main approaches to key management are key predistribution, key transport, key arbitration, and key agreement.

## Slide 32
Key Predistribution:
Key predistribution, as the name suggests, involves distributing keys to all interested parties before the start of communication.
This method involves much less communication and computation, but all participants must be known a priori, during the initial configuration.
Once deployed, there is no mechanism to include new members in the group or to change the key.
As an improvement over the basic predistribution scheme, sub-groups may be formed within the group, and some communication can be restricted to a subgroup.
However, the formation of sub-groups is also an a priori decision with no flexibility during the operation.

## Slide 33
Key Transport:
In key transport systems, one of the communicating entities generates keys and transports them to the other members. The simplest scheme assumes that a shared key already exists among the participating members.
This prior shared key is used to encrypt a new key and is transmitted to all corresponding nodes.
Only those nodes which have the prior shared key can decrypt it. This is called the key encrypting key (KEK) method.
However, the existence of a prior key cannot always be assumed. If the public key infrastructure (PKI) is present, the key can be encrypted with each participant's public key and transported to it. This assumes the existence of a TTP, which may not be available for ad hoc wireless networks.

## Slide 34
Key Arbitration:
Key arbitration schemes use a central arbitrator to create and distribute keys among all participants. Hence, they are a class of key transport schemes.
Networks which have a fixed infrastructure use the AP as an arbitrator, since it does not have stringent power or computation constraints.
In ad hoc wireless networks, the problem with implementation of arbitrated protocols is that the arbitrator has to be powered on at all times to be accessible to all nodes.

## Slide 35
Key Agreement
Most key agreement schemes are based on asymmetric key algorithms.
They are used when two or more people want to agree upon a secret key, which will then be used for further communication.
Key agreement protocols are used to establish a secure context over which a session can be run, starting with many parties who wish to communicate and an insecure channel.
In group key agreement schemes, each participant contributes a part to the secret key. These need the least amount of pre-configuration, but such schemes have high computational complexity.
The most popular key agreement schemes use the Diffie-Hellman exchange, an asymmetric key algorithm based on discrete logarithms

## Slide 36: SECURE ROUTING IN AD HOC WIRELESS NETWORKS
Unlike the traditional wired Internet, where dedicated routers controlled by the Internet service providers (ISPs) exist, in ad hoc wireless networks, nodes act both as regular terminals (source or destination) and also as routers for other nodes. In the absence of dedicated routers, providing security becomes a challenging task in these networks

## Slide 37: Requirements of a Secure Routing Protocol for Ad Hoc Wireless Networks
• Detection of malicious nodes: A secure routing protocol should be able to detect the presence of malicious nodes in the network and should avoid the participation of such nodes in the routing process. Even if such malicious nodes participate in the route discovery process, the routing protocol should choose paths that do not include such nodes.
• Guarantee of correct route discovery: If a route between the source and the destination nodes exists, the routing protocol should be able to find the route, and should also ensure the correctness of the selected route.

## Slide 38
• Confidentiality of network topology: an information disclosure attack may lead to the discovery of the network topology by the malicious nodes. Once the network topology is known, the attacker may try to study the traffic pattern in the network. If some of the nodes are found to be more active compared to others, the attacker may try to mount (e.g., DoS) attacks on such bottleneck nodes. This may ultimately affect the on-going routing process. Hence, the confidentiality of the network topology is an important requirement to be met by the secure routing protocols.
• Stability against attacks: The routing protocol must be self-stable in the sense that it must be able to revert to its normal operating state within a finite amount of time after a passive or an active attack. The routing protocol should take care that these attacks do not permanently disrupt the routing process

## Slide 39: Security-Aware Ad Hoc Routing Protocol
The security-aware ad hoc routing (SAR) protocol uses security as one of the key metrics in path finding.
A framework for enforcing and measuring the attributes of the security metric has to be taken into account .
This framework also enables the use of different levels of security for different applications that use SAR for routing.
In ad hoc wireless networks, communication between end nodes through possibly multiple intermediate nodes is based on the fact that the two end nodes trust the intermediate nodes.

## Slide 40
SAR defines level of trust as a metric for routing and as one of the attributes for security to be taken into consideration while routing.

## Slide 41: PART-B SENSOR NETWORK PLATFORMS AND TOOLS
Introduction:
A real-world sensor network application most likely has to incorporate all these elements, subject to energy, bandwidth, computation, storage, and real-time constraints
There are two types of programming for sensor networks, those carried out by end users and those performed by application developers.

## Slide 42
End User:
An end user may view a sensor network as a pool of data and interact with the network via queries.
Just as with query languages for database systems like SQL good sensor network programming language should be expressive enough to encode application logic at a high level of abstraction
At the same time be structured enough to allow efficient execution on the distributed platform.

## Slide 43
Application Developer:
an application developer must provide end users of a sensor network with the capabilities of data acquisition, processing, and storage.
Unlike general distributed or database systems, collaborative signal and information processing (CSIP) software comprises reactive, concurrent, distributed programs running on ad hoc, resource-constrained, unreliable computation and communication platforms.

## Slide 44: Sensor Node Hardware
Sensor node hardware can be grouped into three categories, each of which entails a different set of trade-offs in the design choices
• Augmented general-purpose computers: Examples include low power PCs, embedded PCs (e.g., PC104), custom-designed PCs (e.g., Sensoria WINS NG nodes),1 and various personal digital assistants (PDA). These nodes typically run off-the-shelf operating systems such as Win CE, Linux, or real-time operating systems and use standard wireless communication protocols such as Bluetooth or IEEE 802.11.

## Slide 45
Compared with dedicated sensor nodes, PC-like platforms are more power hungry. However, when power is not an issue, these platforms have the advantage that they can leverage the availability of fully supported networking protocols, popular programming languages, middleware, and other off-the-shelf software

## Slide 46
• Dedicated embedded sensor nodes: Examples include the Berkeley mote family, the UCLA Medusa family, Ember nodes,2 and MIT μAMP. These platforms typically use commercial off-the-shelf (COTS) chip sets with emphasis on small form factor, low power processing and communication, and simple sensor interfaces. Because of their COTS CPU, these platforms typically support at least one programming language, such as C.

## Slide 47
However, in order to keep the program footprint small to accommodate their small memory size, programmers of these platforms are given full access to hardware but barely any operating system support.
A classical example is the Tiny OS platform and its companion programming language, nesC. We will discuss these platforms in Sections 8.3.1 and 8.3.2.

## Slide 48
• System-on-chip (SoC) nodes: Examples of SoC hardware include smart dust, the BWRC picoradio node, and the PASTA node.3 Designers of these platforms try to push the hardware limits by fundamentally rethinking the hardware architecture trade-offs for a sensor node at the chip design level. The goal is to find new ways of integrating CMOS, MEMS, and RF technologies to build extremely low power and small footprint sensor nodes that still provide certain sensing, computation, and communication capabilities.

## Slide 49: Berkeley Motes
The Berkeley motes are a family of embedded sensor nodes sharing roughly the same architecture.

## Slide 50: MICA mote architecture

## Slide 51: Power consumption of MICA motes

## Slide 52: Sensor Network Programming Challenges
Traditional programming technologies rely on operating systems to provide abstraction for processing, I/O, networking, and user interaction hardware, When applying such a model to programming networked embedded systems, such as sensor networks, the application programmers need to explicitly deal with message passing, event synchronization, interrupt handing, and sensor reading.
As a result, an application is typically implemented as a finite state machine (FSM) that covers all extreme cases: unreliable communication channels, long delays, irregular arrival of messages, simultaneous events, and so on. In a target tracking application implemented on a Linux operating system and with directed diffusion routing, roughly 40 percent of the code implements the FSM and the glue logic of interfacing computation and communication

## Slide 53
For resource-constrained embedded systems with real-time requirements, several mechanisms are used in embedded operating systems to reduce code size, improve response time, and reduce energy consumption.
Microkernel technologies modularize the operating system so that only the necessary parts are deployed with the application.
Real-time scheduling allocates resources to more urgent tasks so that they can be finished early.

## Slide 54: Traditional embedded system programming interface

## Slide 55
• Sensor networks are large-scale distributed systems, where global properties are derivable from program execution in a massive number of distributed nodes. Distributed algorithms themselves are hard to implement, especially when infrastructure support is limited due to the ad hoc formation of the system and constrained power, memory, and bandwidth resources.
• As sensor nodes deeply embed into the physical world, a sensor network should be able to respond to multiple concurrent stimuli at the speed of changes of the physical phenomena of interest. In the rest of the chapter, we give several examples of sensor network software design platforms. We discuss them in terms of both design methodologies and design platforms. A design methodology implies a conceptual model for programmers, with associated techniques for problem decomposition for the software designers.

## Slide 56: Node-Level Software Platforms
Most design methodologies for sensor network software are node centric, where programmers think in terms of how a node should behave in the environment.
A node-level platform can be a node centric operating system, which provides hardware and networking abstractions of a sensor node to programmers, or it can be a language platform, which provides a library of components to programmers.
A typical operating system abstracts the hardware platform by providing a set of services for applications, including file management, memory allocation, task scheduling, peripheral device drivers, and networking.
For embedded systems, due to their highly specialized applications and limited resources, their operating systems make different trade-offs when providing these services.
For example, if there is no file management requirement, then a file system is obviously not needed. If there is no dynamic memory allocation, then memory management can be simplified. If prioritization among tasks is critical, then a more elaborate priority scheduling mechanism may be added.

## Slide 57
TinyOS and TinyGALS are two representative examples of node-level programming tools that we will cover in detail in this section. Other related software platforms include Maté, a virtual machine for the Berkeley motes. Observing that operations such as polling sensors and accessing internal states are common to all sensor network application, Maté defines virtual machine instructions to abstract those operations. When a new hardware platform is introduced with support for the virtual machine, software written in the Maté instruction set does not have to be rewritten.

## Slide 58: Operating System: TinyOS
TinyOS aims at supporting sensor network applications on resource constrained hardware platforms, such as the Berkeley motes.
To ensure that an application code has an extremely small footprint, TinyOS chooses to have no file system, supports only static memory allocation, implements a simple task model, and provides minimal device and networking abstractions.
Furthermore, it takes a language-based application development approach, to be discussed later, so that only the necessary parts of the operating system are compiled with the application.
To a certain extent, each TinyOS application is built into the operating system.

## Slide 59
Like many operating systems, TinyOS organizes components into layers.
Intuitively, the lower a layer is, the “closer” it is to the hardware; the higher a layer is, the “closer” it is to the application.
In addition to the layers, TinyOS has a unique component architecture and provides as a library a set of system software components.
A component specification is independent of the component implementation.
Although most components encapsulate software functionalities, some are just thin wrappers around hardware.

## Slide 60: FieldMonitor application for sensing and sending measurements

## Slide 61: Imperative Language: nesC
nesC is an extension of C to support and reflect the design of TinyOS v1.0 and above. It provides a set of language constructs and restrictions to implement TinyOS components and applications.
Component Interface
A component in nesC has an interface specification and an implementation. To reflect the layered structure of TinyOS, interfaces of a nesC component are classified as provides or uses interfaces. A provides interface is a set of method calls exposed to the upper layers, while a uses interface is a set of method calls hiding the lower layer components. Methods in the interfaces can be grouped and named.

## Slide 62: The interface definition of the Timer component in nesC

## Slide 63
Component Implementation
There are two types of components in nesC, depending on how they are implemented: modules and configurations. Modules are implemented by application code (written in a C-like syntax). Configurations are implemented by connecting interfaces of existing components.
The implementation part of a module is written in C-like code.
A command or an event bar in an interface foo is referred as foo.bar.
A keyword call indicates the invocation of a command.
A keyword signal indicates the triggering by an event.

## Slide 64: The implementation definition of the Timer component in nesC.

## Slide 65
Concurrency and Atomicity
The language nesC directly reflects the TinyOS execution model through the notion of command and event contexts.
To prevent some state from being updated by both scheduled tasks and event-triggered interrupt handlers, nesC provides language facilities to limit the race conditions among these operations.
In nesC, code can be classified into two types:
Asynchronous code (AC): Code that is reachable from at least one interrupt handler.
Synchronous code (SC): Code that is only reachable from tasks. Because the execution of TinyOS tasks are nonpreemptive and interrupt handlers preempts tasks, SC is always atomic with respect to other SCs.

## Slide 66: Dataflow-Style Language: TinyGALS
Dataflow languages are intuitive for expressing computation on interrelated data units by specifying data dependencies among them.
A dataflow program has a set of processing units called actors. Actors have ports to receive and produce data, and the directional connections among ports are FIFO queues that mediate the flow of data.
Actors in dataflow languages intrinsically capture concurrency in a system, and the FIFO queues give a structured way of decoupling their executions.
The execution of an actor is triggered when there are enough input data at the input ports.
Asynchronous event-driven execution can be viewed as a special case of dataflow models, where each actor is triggered by every incoming event. The globally asynchronous and locally synchronous (GALS) mechanism is a way of building event-triggered concurrent execution from thread-unsafe components. TinyGALS is such a language for TinyOS.

## Slide 67
TinyGALS Programming Model
TinyGALS supports all TinyOS components, including its interfaces and module implementations. All method calls in a component interface are synchronous method calls—that is, the thread of control enters immediately into the callee component from the caller component.
An application in TinyGALS is built in two steps:
(1) constructing asynchronous actors from synchronous components, and
(2) constructing an application by connecting the asynchronous components though FIFO queues. An actor in TinyGALS has a set of input ports, a set of output ports, and a set of connected TinyOS components.

## Slide 68
TinyGALS Code Generation
TinyGALS takes a generative approach to mapping high-level constructs such as FIFO queues and actors into executables on Berkeley motes. Given the highly structured architecture of TinyGALS applications, efficient scheduling and event handling code can be automatically generated to free software developers from writing error-prone concurrency control code.
The rest of this section discusses a code generation tool that is implemented based on TinyOS v0.6.1 for Berkeley motes.
Given the definitions for the components, actors, and application, the code generator automatically generates all of the necessary code for (1) component links and actor connections, (2) application initialization and start of execution, (3) communication among actors, and (4) global variable reads and writes

## Slide 69: Node-Level Simulators
Node-level design methodologies are usually associated with simulators that simulate the behavior of a sensor network on a per-node basis. Using simulation, designers can quickly study the performance (in terms of timing, power, bandwidth, and scalability) of potential algorithms without implementing them on actual hardware and dealing with the vagaries of actual physical phenomena. A node-level simulator typically has the following components:
• Sensor node model: A node in a simulator acts as a software execution platform, a sensor host, as well as a communication terminal. In order for designers to focus on the application-level code, a node model typically provides or simulates a communication protocol stack, sensor behaviors (e.g., sensing noise), and operating system services. If the nodes are mobile, then the positions and motion properties of the nodes need to be modeled. If energy characteristics are part of the design considerations, then the power consumption of the nodes needs to be modeled.

## Slide 70
Communication model: Depending on the details of modeling, communication may be captured at different layers. The most elaborate simulators model the communication media at the physical layer, simulating the RF propagation delay and collision of simultaneous transmissions.
Physical environment model: A key element of the environment within which a sensor network operates is the physical phenomenon of interest. The environment can also be simulated at various levels of detail. For example, a moving object in the physical world may be abstracted into a point signal source. The motion of the point signal source may be modeled by differential equations or interpolated from a trajectory profile. If the sensor network is passive—that is, it does not impact the behavior of the environment—then the environment can be simulated separately or can even be stored in data files for sensor nodes to read in

## Slide 71
Statistics and visualization: The simulation results need to be collected for analysis. Since the goal of a simulation is typically to derive global properties from the execution of individual nodes, visualizing global behaviors is extremely important. An ideal visualization tool should allow users to easily observe on demand the spatial distribution and mobility of the nodes, the connectivity among nodes, link qualities, end-to-end communication routes and delays, phenomena and their spatio-temporal dynamics, sensor readings on each node, sensor node states, and node lifetime parameters

## Slide 72: The ns-2 Simulator and its Sensor Network Extensions
The simulator ns-2 is an open-source network simulator that was originally designed for wired, IP networks. Extensions have been made to simulate wireless/mobile networks (e.g., 802.11 MAC and TDMA MAC) and more recently sensor networks. While the original ns-2 only supports logical addresses for each node, the wireless/mobile extension of it introduces the notion of node locations and a simple wireless channel model. This is not a trivial extension, since once the nodes move, the simulator needs to check for each physical layer event whether the destination node is within the communication range. For a large network, this significantly slows down the simulation speed.

## Slide 73
The Simulator TOSSIM
TOSSIM is a dedicated simulator for TinyOS applications running on one or more Berkeley motes. The key design decisions on building TOSSIM were to make it scalable to a network of potentially thousands of nodes, and to be able to use the actual software code in the simulation. To achieve these goals, TOSSIM takes a cross-compilation approach that compiles the nesC source code into components in the simulation. The event-driven execution model of TinyOS greatly simplifies the design of TOSSIM. By replacing a few low-level components, such as the A/D conversion (ADC), the system clock, and the radio front end, TOSSIM translates hardware interrupts into discreteevent simulator events. The simulator event queue delivers the interrupts that drive the execution of a node. The upper-layer TinyOS code runs unchanged.

## Slide 74: Programming Beyond Individual Nodes: State-Centric Programming
Many sensor network applications, such as target tracking, are not simply generic distributed programs over an ad hoc network of energy-constrained nodes. Deeply rooted in these applications is the notion of states of physical phenomena and models of their evolution over space and time. Some of these states may be represented on a small number of nodes and evolve over time, while others may be represented over a large and spatially distributed number of nodes, as in tracking a temperature contour.
A distinctive property of physical states, such as location, shape, and motion of objects, is their continuity in space and time. Their sensing and control is typically done through sequential state updates

## Slide 75
Collaboration Groups
A collaboration group is a set of entities that contribute to a state update. These entities can be physical sensor nodes, or they can be more abstract system components such as virtual sensors or mobile agents hopping among sensors. In this context, they are all referred to as agents. Intuitively, a collaboration group provides two abstractions: its scope to encapsulate network topologies and its structure to encapsulate communication protocols. The scope of a group defines the membership of the nodes with respect to the group. For the discussion of collaboration groups in this chapter, we broaden the notion of nodes to include both physical sensor nodes and virtual sensor nodes that may not be attached to any physical sensor.

## Slide 76
Examples of Groups
Combinations of scopes and structures create patterns of groups that may be highly reusable from application to application. Here, we give several examples of groups, though by no means is it a complete list. The goal is to illustrate the wide variety of the kinds of groups, and the importance of mixing and matching them in applications.
Geographically Constrained Group. A geographically constrained group (GCG) consists of members within a prespecified geographical extent. Since physical signals, especially the ones from point targets, may propagate only to a limited extent in an environment, this kind of group naturally represents all the sensor nodes that can possibly “sense” a phenomenon

## Slide 77
N-hop Neighborhood Group. When the communication topology is more important than the geographical extent, hop counts are useful to constrain group membership. An n-hop neighborhood group (n-HNG) has an anchor node and defines that all nodes within n communication hops are members of the group.
Publish/Subscribe Group. A group may also be defined more dynamically, by all entities that can provide certain data or services, or that can satisfy certain predicates over their observations or internal states
Acquaintance Group. An even more dynamic kind of group is the acquaintance group (AG), where a member belongs to the group because it was “invited” by another member in the group. The relationships among the members may not depend on any physical properties at the current time but may be purely logical and historical.

## Slide 78: PIECES: A State-Centric Design Framework
PIECES (Programming and Interaction Environment for Collaborative Embedded Systems) is a software framework that implements the methodology of state-centric programming over collaboration groups to support the modeling, simulation, and design of sensor network applications. It is implemented in a mixed Java-Matlab environment.
Principals and Port Agents
PIECES comprises principals and port agents. Figure 8.16 shows the basic relations among principals and port agents. A principal is the key component for maintaining a piece of state. Typically, a principal maintains state corresponding to certain aspects of the physical phenomenon of interest.

## Slide 79
Principal Groups
Principals can form groups. A principal group gives its members a means to find other relevant principals and attaches port agents to them. A principal may belong to multiple groups. A port agent, however, serving as a proxy for a principal in the group, can only be associated with one group
Mobility
A principal is hosted by a specific network node at any given time. The most primitive type of principal is a sensing principal, which is fixed to a sensor node. A sensing principal maintains a piece of (local) state related to the physical phenomenon, based solely on its own local measurement history.
PIECES Simulator
PIECES provides a mixed-signal simulator that simulates sensor network applications at a high level. The simulator is implemented using a combination of Java and Matlab. An event-driven engine is built in Java to simulate network message passing and agent execution at the collaboration-group level. A continuous-time engine is built in Matlab to simulate target trajectories, signals and noise, and sensor front ends. The main control flow is in Java, which maintains the global notion of time.

## Slide 80: Multitarget Tracking Problem Revisited
Using the state-centric model, programmers decouple a global state into a set of independently maintained pieces, each of which is assigned a principal. To update the state, principals may look for inputs from other principals, with sensing principals supporting the lowest-level sensing and estimation tasks. Communication patterns are specified by defining collaboration groups over principals and assigning corresponding roles for each principal through port agents.

## Slide 81: PART-C APPLICATIONS of WSN
INTRODUCTION:
It is expected that by the end of this decade, the predominant mode of Internet access will be over wireless networks. In order to support high data rates on short ranges, new promising technologies such as the ultra-wide band (UWB) transmission scheme and optical wireless wavelength division multiplexing (WDM) networks are currently under research.
In addition to the demands on increasing the performance of the lower layers of the system, pressure is on to efficiently reuse the existing frequencies, which also demands allocation of newer bands for commercial wireless communications.
The additional areas of interest in next-generation wireless networks include freedom in selection of a particular network from a set of heterogeneous wireless networks, seamless handoff across such networks, support for multimedia traffic, and all the above services at an affordable cost.

## Slide 82: ULTRA-WIDE-BAND RADIO COMMUNICATION
The major differences between the ultra-wide band (UWB) technology and the existing narrow-band and wide-band technologies are the following:
(i) The bandwidth of UWB systems, as defined by the Federal Communications Commission (FCC), is more than 25% of the center frequency or a bandwidth greater than 500 MHz.
(ii) The narrow-band and wide-band technologies make use of a radio frequency (RF) carrier to shift the base band signal to the center of the carrier frequency, whereas the UWB systems are implemented in a carrier less fashion in which the modulation scheme can directly modulate base band signals into an impulse with very sharp rise and fall time, thus resulting in a waveform ranging several GHz of bandwidth.

## Slide 83
A simple example of UWB transmission is any radio frequency (RF) transmission with a bandwidth of 500 MHz at a center frequency of 2GHz.
The principles behind the operation of UWB technology had been applied in radar applications since the 1980s.
With proper emission restrictions (restrictions on the upper limit on the transmission power) in place, the UWB spectrum can overlay the existing narrow-band spectrum, resulting in much more efficient use of the existing radio spectrum.

## Slide 84
Figure shown illustrates the upper limits of transmission power permitted for the UWB system in comparison with the IEEE 802.11a. The 802.11a standard has three bands, each with 100 MHz bandwidth with an upper limit of effective isotropically radiated power (EIRP)

## Slide 85
Operation of UWB Systems
The operation of UWB systems is based on transmission of ultra-short pulses (that yields a wide-band bandwidth signal) which are also called monocycles. Each monocycle is similar to a single cycle of an ultra-high frequency sine wave and is a single ultra-short pulse. The pulse widths of monocycles range from 0.10 to 1.6 ns with pulse-to-pulse intervals of between 25 and 1,000 ns. A single monocycle of width 0.5 ns is shown in Figure below

## Slide 86
Comparison of UWB with Other Technologies
The trends that drive the short-range wireless technologies, including UWB technology, are the following:
(i) The growing demand for data and multimedia capability in portable devices at high data rate but at low cost and power consumption.
(ii) Increasing pressure on the wireless spectrum demanding higher reuse.
(iii) Decreasing semiconductor cost and availability of low-power devices. Some of the competing technologies for such wireless access scenario are IEEE 802.11b, IEEE 802.11a, and Bluetooth.

## Slide 87
Major Issues in UWB
With the evolution of wireless networks with higher data rates, similar advancement in all the layers of protocol stack is required to make use of the high data rates provided by the physical layers. The increasing application space for multimedia communications puts additional requirements on latency and delay performances. The error-prone and time-varying nature of wireless link results in large delay, delay variations, and misordering of packets. In this section, the major issues at the physical and MAC layers are discussed

## Slide 88
The most important issues in the design of MAC-layer protocol for UWB systems are the following:
(i) controlling channel access
(ii) maintaining QoS
(iii) providing security. In addition to these, the design of MAC protocols for UWB systems is dictated by other properties of UWB. For example, UWB systems have unique features such as precise timing or position information. The position information can be obtained by the following feature. A 10 GHz UWB system can distinguish signal echos (signal echos refer to the multipath signals that arrive at the receiver through different paths with corresponding delays) that differ by 100 picoseconds.

## Slide 89
Advantages and Disadvantages of UWB
Promising applications of UWB in communication include cable-free audio/video devices, broadband WPANs, and high-speed wireless links. UWB systems are potential candidates for high data rate, low power, and short- to medium-range communication applications. UWB systems have a wide range of applications other than communications, some of which are automobile collision-detection devices, medical imaging similar to x-rays and ultrasound scans, through-wall imaging for detecting people and objects in law enforcement applications, and ground-penetrating radars
The major advantages of UWB systems include simplicity of implementation, high data rate, inherent robustness to multipath fading, flexibility of operation, low power consumption, and low cost of implementation. The disadvantages of UWB systems include stringent design requirements of communication subsystems and chances of interference from the existing technologies.

## Slide 90: WIRELESS FIDELITY SYSTEMS
Wireless fidelity (Wi-Fi) system is the high-speed wireless LAN that was originally intended to extend the wired Ethernet in offices to wireless clients.
The coverage area and ability to support high bit rates are the two major reasons behind the name Wi-Fi.
Though the popular wireless LAN standards IEEE802.11b and 802.11a are considered as the standard Wi-Fi candidates, conceptually any high-speed wireless LAN protocol such as HiperLAN can be used.
The integration of Wi-Fi hotspots (wireless LAN access points) with wide area wireless networking technologies such as GSM and GPRS provides an added advantage for the mobile nodes.

## Slide 91
The Service Provider Models for Wi-Fi Systems
• The Wi-Fi micro carrier model: In this model, small business operators can set up their own access points (APs) and maintain customer relations and billing with subscribers. An example of this category is a restaurant operating a small Wi-Fi system with a set of APs on its premises.
• The franchisee-franchisor model: This model for Wi-Fi systems is that a franchisor company making an agreement with a franchisee (e.g., a restaurant which has an inbuilt Wi-Fi system for its internal purposes) for providing Wi-Fi connectivity on a revenue-sharing basis. The external communication, access network costs, and back-office softwares may be supplied and maintained by the franchisor. Hence, the franchisor company can extend its services to the public.
• The Wi-Fi carrier model: In this model, a particular company referred to as Wi-Fi carrier can own, deploy, and operate a number of Wi-Fi system-enabled APs at public places. The subscribers can utilize the designated carrier's network services in their coverage area based on acceptable billing models.

## Slide 92
• The Wi-Fi aggregator model: This model refers to an abstract service provider which strikes wholesale partnerships with Wi-Fi operators. Such aggregators mainly focus on two major things: (i) reselling of the services provided by the Wi-Fi operators and (ii) giving their subscribers access to a large number of networks. The advantages of this model are easy scale-up of network coverage as the aggregator does not own the infrastructure and hence, by having more partnerships, a service provider can increase the coverage area and the customer base.
• The extended service provider model: The synergistic operation of Wi-Fi systems with existing cellular systems, especially with the 3G systems, can increase profits for cellular operators. This can even lead to reduction in the deployment cost of 3G systems. The widespread deployment of Wi-Fi systems can be considered as complementing the 3G systems.

## Slide 93
The extended service provider model: The synergistic operation of Wi-Fi systems with existing cellular systems, especially with the 3G systems, can increase profits for cellular operators. This can even lead to reduction in the deployment cost of 3G systems. The widespread deployment of Wi-Fi systems can be considered as complementing the 3G systems. Also, the availability of wireless devices equipped with Wi-Fi and cellular interfaces encourages the possibility of switching to the Wi-Fi systems whenever an AP is detected.

## Slide 94: Issues in Wi-Fi Systems
Security
Security in Wi-Fi systems is important and requires viable solutions. The IEEE has proposed a long-term security architecture for 802.11, which is referred to as robust security network (RSN). The major objectives of RSN, which is based on IEEE 802.1x, are access control, authentication, and key management.

## Slide 95
A typical scenario
of a Wi-Fi system.

## Slide 96
The eavesdropper: Wireless medium is inherently broadcast, making it trivial for the adversary with a good receiver to eavesdrop on other stations' traffic. The use of a single key for encryption proved inadequate for this purpose. Dynamic changing of the encryption key is a must for making the eavesdropping a difficult task. Since the majority of the Wi-Fi systems are not WEP (wired equivalent privacy – any privacy solution in which the effort required to break the cipher is expected to be roughly equivalent to the effort required by an intruder to tap into a wired Ethernet)-enabled, it is easier for an inexperienced hacker to snoop on valuable information such as credit card number, PIN numbers, or social security numbers from a public hot spot Wi-Fi system

## Slide 97
The rogue client: The authenticated client that has intentions of acting against the organization is another problem aggravated by the wireless environment. A Wi-Fi client running a routing protocol and an additional wired interface can easily use its authentication information on its corporate wireless network infrastructure to transfer valuable information. This problem is extremely difficult to trace and prevent as the loss incurred cannot easily be detected.
• The rogue AP: The rogue AP is the unauthorized AP attached to an organization's network, either on its premises or in its authorized employee's home. An AP without the necessary security provisions, or in situations where the security is disabled temporarily, can act as a rogue AP. Even with security features such as WEP, organizations that use virtual private network (VPN) to secure their wireless LANs may be compromising valuable data. A VPN is a communication network between two or more machines or networks, built for the private use of an organization over a shared public infrastructure such as the Internet.

## Slide 98
Session hijack attack: In this case, a hijacker node waits until the successful completion of a node's authentication process with an AP. On completion of the authentication, the hijacker sends a forged disassociate message that appears to be originated by the AP. On reception of the message, the original node gets disassociated. The AP continues to consider the node as part of the network. Now the hijacker, using the originally authenticated node's address, can utilize network services until the session expires.
• Man-in-the-middle attack: When an adversary spoofs messages to represent itself as AP to a node under attack, it can obtain the victim's authentication information. Using this information, the adversary authenticates with another AP masquerading as the victim node. This attack is known as man-in the-middle attack. This attack is particularly effective when the victim node is not present within the transmission range of the AP.

## Slide 99
Authentication
The IEEE 802.1x standard is proposed for providing authentication and controlling traffic to a protected network, as well as for dynamically changing encryption keys. The use of the extendible authentication protocol (EAP) as a framework for wired and wireless network provides a mechanism for multiple authentication methods such as certificate-based authentication

## Slide 100
Quality of Service (QoS)
Provisioning of QoS is important in supporting time-sensitive traffic such as voice and video. The IEEE802.11e standard which is under consideration is aiming at providing enhanced QoS for Wi-Fi systems.
Economics of Wi-Fi
• Billing schemes: Billing for Wi-Fi systems assumes importance as the commercial viability is a major factor for the existence of the Wi-Fi systems. The possible billing schemes include the following. The entity that has the responsibility of customer care and billing can be different from the one which actually provides network access service. Such an agency is referred to as a billing agency.

## Slide 101
• Revenue sharing model: In the franchisee-franchisor model and the aggregator model, the sharing of revenue is important as there exist multiple business entities in the process of customer relationship, billing, and providing service. Different revenue-sharing models that include a fixed fraction-sharing model (in which the amount shared among the parties involved is prefixed) and a variable-fraction volume-based sharing model (in which the percentage of revenue that goes to different parties involved varies with the volume of data transferred) can be employed.

## Slide 102
Spectrum Issues
The issues related to spectrum management are important as Wi-Fi becomes popular with its increasing use as a critical business communication infrastructure. The current allocation of free ISM band in the 2.4 GHz band for 802.11b raises several questions of interference. The source of interferences can be either naturally generated by other devices that are designated to operate at the same band or artificially generated by a rogue interference generator node. Since ISM band is unlicensed, any user with an 802.11 interface can disrupt communication at a specific location without inviting prosecution.
The major interference sources for Wi-Fi systems are the following: (i) interference from cordless phones, microwave ovens, and Bluetooth-enabled devices and (ii) interference from jammers

## Slide 103: Future Research Directions
As sensors, actuators, embedded processing, and wireless become ubiquitous, we need new ways to network, organize, query, and program them.
Secure Embedded Systems
Ensuring security and privacy is one of the highest priorities for sensor network systems. Whether they are designed for commercial applications such as vehicle-to-vehicle safety-related communications or for military battlefield monitoring applications, one must authenticate the source of data to prevent the malicious injection of bogus data. We need to adapt existing public key infrastructure (PKI) for sensor networks or develop new protocols that are lightweight and can be implemented on resource-limited sensor nodes. In some cases, asymmetric protocols may be preferable since base stations or cluster leader nodes have more computational capability and energy supply than other sensing nodes.

## Slide 104
Programming Models and Embedded Operating Systems
In a typical embedded software (EmSoft) application today, half of the code may be dedicated to management of threads, events, messages, or timing issues, and not with the application itself. How can an application developer, without an extensive computer science background in networking and embedded software, easily write software for a network of thousands of embedded devices? Needed is a new breed of embedded operating systems and design environments that provide a mental model closer to the way people think about these applications

## Slide 105
Management of Collaborative Groups
The ability to form dynamic, ad hoc groups of nodes according to the requirements of a sensing task and resource availability is at the center of many sensor network systems and applications. We will need networking protocols for nodes participating in a group to maintain communications despite mobility or node and link failure. A key consideration in the design is to minimize unnecessary energy and bandwidth usage. Anticipated usage patterns and data rates may determine whether it should be infrastructure-based or infrastructure-less (e.g., using source-initiated ad hoc routing).

## Slide 106
Lightweight Signal Processing
Lightweight signal processing algorithms refer to methods that require relatively little floating- point computation and less memory storage than those that are floating-point intensive such as Fast Fourier Transform (FFT). This is attractive, since the signal processing algorithms are targeted for resource-limited nodes such as the Berkeley motes.

## Slide 107
Networks of High-Data-Rate Sensors
Though most of the examples we have discussed deal with low data rate sensors, such as acoustic microphones, there is increasing interest in networking high-data-rate sensors as well, such as cameras and other imagers. The sheer volume of data generated by such sensors makes it imperative to extract and transmit high-level descriptions of what is sensed, as opposed to raw signals. Further, the data sensed by nearby sensors is often highly correlated; such redundancy must be detected and removed—here distributed data compression techniques come into play. Unlike the usual compression scenario of, say, broadcasting a video signal, where the compressor can be an expensive algorithm while decompressors must be cheap, here the roles are reversed.

## Slide 108
Google® for the Physical World
Interacting with a distributed sensor system requires research in user interface and search engines that are different from those for IP-based networks. Since the primary purpose of a sensing system is to gather information, we’d like to be able to “browse” and ask high-level questions about the physical environment. Instead of asking moisture sensor #153 for its current reading, why not query the lawn to see if it needs more water? What is needed is an XML-like language for sensor networks, and search techniques for matching higher-level queries with physical signals. In some cases, the search may trigger additional sensing actions.

## Slide 109
Closing the Loop with Actuators
In many application scenarios, the sensors are the “eyes” that inform the “hands” and “legs” what to do. The hands and legs are the actuators. For example, moisture sensors may sense that a patch of green is dry and use the information to command the sprinklers near that spot. Or, sensors may be on wheels, and can move to different locations, thus providing an extra degree of freedom in sensor placement. Common to these problems are the tight coupling between sensing, decision making, and actuation.

## Slide 110
Distributed Information Architecture
Distributed information architectures deal with how information is organized and manipulated in a sensor network. An inference task typically is more complex than finding the maximum or average of sensor values. It may involve reasoning about motion or relations about observed phenomena. A key problem is distributed inference, mapping representations and techniques such as graphical models or dynamic Bayesian networks to sensor networks

## Slide 111: Smart meter
A smart meter is usually an electronic device that records consumption of electric energy in intervals of an hour or less and communicates that information at least daily back to the utility for monitoring and billing. Smart meters enable two-way communication between the meter and the central system. Unlike home energy monitors, smart meters can gather data for remote reporting. Such an advanced metering infrastructure (AMI) differs from traditional automatic meter reading (AMR) in that it enables two-way communications with the meter

## Slide 112
Overview
The term Smart Meter often refers to an electricity meter, but it also may mean a device measuring natural gas or water consumption. Similar meters, usually referred to as interval or time-of-use meters, have existed for years, but "Smart Meters" usually involve real-time or near real-time sensors, power outage notification, and power quality monitoring. These additional features are more than simple automated meter reading (AMR). They are similar in many respects to Advanced Metering Infrastructure (AMI) meters. Interval and time-of-use meters historically have been installed to measure commercial and industrial customers, but may not have automatic reading.

## Slide 113
Brief history
In 1972, Theodore George “Ted” Paraskevakos, while working with Boeing in Huntsville, Alabama, developed a sensor monitoring system which used digital transmission for security, fire and medical alarm systems as well as meter reading capabilities for all utilities. This technology was a spin-off of the automatic telephone line identification system, now known as Caller ID. In 1974, Mr. Paraskevakos was awarded a U.S. patent for this technology. In 1977, he launched Metretek, Inc., which developed and produced the first fully automated, commercially available remote meter reading and load management system. Since this system was developed pre-Internet, Metretek utilized the IBM series mini-computer. For this approach, Mr. Paraskevakos and Metretek were awarded multiple patents.

## Slide 114
Purpose
Since the inception of electricity deregulation and market-driven pricing throughout the world, utilities have been looking for a means to match consumption with generation. Traditional electrical and gas meters only measure total consumption, and so provide no information of when the energy was consumed at each metered site. Smart meters provide a way of measuring this site-specific information, allowing utility companies to introduce different prices for consumption based on the time of day and the season.

## Slide 115
Technology
Of all smart meter technologies, one critical technological problem is communication. Each meter must be able to reliably and securely communicate the information collected to some central location. Considering the varying environments and locations where meters are found, that problem can be daunting. Among the solutions proposed are: the use of cell and pager networks, satellite, licensed radio, combination licensed and unlicensed radio, and power line communication. Not only the medium used for communication purposes, but also the type of network used, is critical. As such, one would find: fixed wireless, mesh network or a combination of the two. There are several other potential network configurations possible, including the use of Wi-Fi and other internet related networks. To date no one solution seems to be optimal for all applications

## Slide 116
Protocols
ANSI C12.18 is an ANSI standard that describes a protocol used for two-way communications with a meter, mostly used in North American markets. The C12.18 standard is written specifically for meter communications via an ANSI Type 2 Optical Port, and specifies lower-level protocol details. ANSI C12.19 specifies the data tables that will be used. ANSI C12.21 is an extension of C12.18 written for modem instead of optical communications, so it is better suited to automatic meter reading.

## Slide 117
Data management
The other critical technology for Smart Meter systems is the information technology at the utility that integrates the Smart Meter networks with the utility applications, such as billing and CIS. This includes the Meter Data Management system. It also is important for Smart Grid implementations that power line communication (PLC) technologies used within the home over a Home Area Network (HAN), are standardized and compatible. The HAN allows HVAC systems and other household appliances to communicate with the smart meter, and from there to the utility

## Slide 118
Security
Implementing security protocols that will protect these devices from malicious attacks and new exploits has been a problematic task. One proposed smart meter data verification method involves analyzing the data in real time to detect anomalies. By identifying exploits as they are being leveraged by attackers, this intrusion detection system (IDS) will mitigate the suppliers' risks of energy theft by consumers and denial-of-service attacks by hackers.

## Slide 119
Examples of Smart metering applications

## Slide 120
Advanced metering infrastructure
Advanced Metering Infrastructure (AMI) are systems that measure, collect, and analyze energy usage, and communicate with metering devices such as electricity meters, gas meters, heat meters, and water meters, either on request or on a schedule. These systems include hardware, software, communications, consumer energy displays and controllers, customer associated systems, Meter Data Management (MDM) software, and supplier business systems. Government agencies and utilities are turning toward advanced metering infrastructure (AMI) systems as part of larger “Smart Grid” initiatives. AMI extends current advanced meter reading (AMR) technology by providing two way meter communications, allowing commands to be sent toward the home for multiple purposes, including “time-of-use” pricing information, demand-response actions, or remote service disconnects.

## Slide 121: Home automation for the elderly and disabled
The form of home automation called assistive domestics focuses on making it possible for older adults and people with disabilities to remain at home, safe and comfortable. Home automation is becoming a viable option for older adults and people with disabilities who would prefer to stay in the comfort of their homes rather than move to a healthcare facility. This field uses much of the same technology and equipment as home automation for security, entertainment, and energy conservation but tailors it towards older adults and people with disabilities

## Slide 122
Advantages
Home automation is being implemented into more and more homes of older adults and people with disabilities in order to maintain their independence and safety. These smart homes allow older adults and people with disabilities to stay in their homes where they feel comfortable, instead of moving to a costly health care facility. The transition to a health care facility can cause a lot of anxiety and home automation can either prevent or delay this anxiety (Cheek 2005). For the disabled smart homes give them opportunity for independence, which will help them gain confidence and determination. Smart homes can provide both older adults and people with disabilities with many different types of emergency assistance systems, security features, fall prevention, automated timers, and alerts.

## Slide 123
Systems
Home automation for healthcare can range from very simple alerts to lavish computer controlled network interfaces. Some of the monitoring or safety devices that can be installed in a home include lighting and motion sensors, environmental controls, video cameras, automated timers, emergency assistance systems, and alerts.
Security
In order to maintain the security of the home many home automation systems integrate features such as remote keyless entry systems which will allow seniors to view who is at the door and then remotely open the door. Home networks can also be programmed to automatically lock doors and shut blinds in order to maintain privacy.

## Slide 124
Reminder systems
Home automation systems may include automatic reminder systems for the elderly (Cheek 2005). Such systems are connected to the Internet and make announcements over an intercom. They can prompt about doctor’s appointments and taking medicine, as well as everyday activities such as turning off the stove, closing the blinds, locking doors, etc. Users choose what activities to be reminded of. The system can be set up to automatically perform tasks based on user activity, such as turning on the lights or adjusting room temperature when the user enters specified areas.

## Slide 125
Medication Dispensing and Spoon-feeding
Smart homes can implement medication dispensing devices in order to ensure that necessary medications are taken at appropriate times (Cheek 2005). Automated pill dispensers can dispense only the pills that are to be taken at that time and are locked; versions are available for Alzheimer’s patients that have a lock on them (Cheek 2005). For diabetic patients a talking glucose monitor allows the patient to check their blood sugar level and take the appropriate injection (Cheek 2005). Digital thermometers are able to recognize a fever and alert physicians. Blood pressure and pulse monitors dispense hypertensive medications when needed. There are also spoon-feeding robots