## Slide 1: Transport Layer protocols for Ad Hoc Wireless Networks
Introduction
Issues
Design Goals
Classifications
TCP Over Ad Hoc Wireless Networks
Other Transport Layer Protocols

## Slide 2: INTRODUCTION
Transport Layer Transport Layer is the fourth layer of OSI reference model. It provided transparent transfer of data between end system using the service of the network layer. Two main protocols are Transmission Control Protocol (TCP) User Datagram Protocol (UDP)
The objectives of a transport layer protocol include setting up of:
End-to-end connection
End-to-end delivery of data packets
Flow control
Congestion control
Click to add text

## Slide 3: Contd..
Transport layer protocols:
User Datagram Protocol (UDP): It is simplest Transport Layer communication protocol available of the TCP/IP protocol suite. It involves minimum amount of communication mechanism. Unreliable and connection-less transport layer protocols. It send short packets of data, called datagrams.
Transmission Control Protocol (TCP): It is one of the main protocols in TCP/IP networks. Whereas the IP protocol deals only with packets, TCP enables two hosts to establish a connection and exchange streams of data. TCP guarantees delivery of data and the delivery in the same order in which they were sent. It is reliable, byte-stream-based, and connection-oriented transport layer protocols.These traditional wired transport layer protocols are not suitable for ad hoc wireless networks.

## Slide 4: Contd..

## Slide 5: Contd..

## Slide 7: ISSUES
Issues while designing a transport layer protocol for ad hoc wireless networks:
Induced traffic refers to the traffic at any given link due to the relay traffic through neighbouring links.
Induced throughput unfairness refers to the throughput unfairness at the transport layer due to the throughput/delay unfairness existing at the lower layers such as the network and MAC layers.
Separation of congestion control, reliability, and flow control could improve the performance of the transport layer.
Power and bandwidth constraints affects the performance of a transport layer protocol.
Misinterpretation of congestion occurs in ad-hoc wireless networks.
Completely decoupled transport layer needs to adapt to the changing network environment.
Dynamic topology affects the performance of a transport layer

## Slide 8: DESIGN GOALS
The protocol should maximize the throughput per connection.
It should provide throughout fairness across contending(challenging/oppose) flows.
It should minimize connection setup and connection maintenance overheads.
The protocol should have mechanisms for congestion control and flow control in the network.
It should be able to provide both reliable and unreliable connections.
The protocol should be able to adapt to the dynamics of the network.
One of the important resources must be used efficiently.
The protocol should be aware of resource constraints.
The protocol should make use of information from the lower layer.
It should have a well-defined cross-layer interaction framework.
The protocol should maintain end-to-end semantics.

## Slide 9: CLASSIFICATION OF TRANSPORT LAYER SOLUTIONS

## Slide 10: TCP OVER AD-HOC WIRELESS NETWORKS:
TCP taking 90% of the traffic is predominant in the Internet.
This chapter focuses on TCP extension in ad hoc wireless networks.
Transport protocol should be independent of the network layer technology, e.g., no matter fiber or radio is used But TCP is optimized for wired network
Congestion control TCP assumes timeout is due to congestion Wireless links are not reliable, packet loss may be as high as 20%
In wired network, packet loss is due to congestion slow down In wireless network, due to wireless links try harder

## Slide 11: WHY DOES TCP NOT PERFORM WELL IN AD-HOC WIRELESS NETWORKS:
Misinterpretation of packet loss
Frequent path breaks
Effect of path length
Misinterpretation of congestion window
Asymmetric link behaviour
Uni-directional path: TCP ACK requires RTS-CTS-Data-ACK exchange
Multipath routing
Network partitioning and remerging
The use of sliding-window-based transmission

## Slide 15: TCP OVER AD HOC WIRELESS NETWORK:
Split-TCP:
provides a unique solution to the channel fairness problem by splitting the transport layer objectives into congestion control and end-to-end reliability.
Splits a long TCP connection into a set of short concatenated TCP connections with a number of selected intermediate nodes as terminating points of these short connections.
Advantages
Improved throughput
Improved throughput fairness
Reduced impact of mobility
Disadvantages
It requires modifications to TCP protocol.
The end-to-end connection handling of traditional TCP is disturbed
.The failure of substitution nodes can lead to throughput degradation.

## Slide 17: TCP OVER AD HOC WIRELESS NETWORK:….cntd
TCP with Explicit Link Failure Notification (TCP-ELFN)
Handle explicit link failure notification
Use TCP probe packets for detecting the route reestablishment.
The ELFN is originated by the node detecting a path break upon detection of a link failure to the TCP sender.

## Slide 18
TCP ELFN Explicit Link Failure Notification (ELFN) contd..
The objective :
To provide the TCP sender with information about link and route failures
TCP sender can avoid responding to the failures as if congestion occurred
DSR’s route failure message is modified
A payload similar to the “host unreachable” ICMP message
The sender and receiver’s addresses and ports and seq number

## Slide 19
Advantages:
improves the TCP performance by decoupling the path break information from the congestion information by the use of ELFN.
Less dependent on the routing protocol and requires only link failure notification
Disadvantages
When the network is partitioned, the path failure may last longer
The congestion window after a new route is obtained may not reflect the achievable transmission rate acceptable to the network and TCP receiver

## Slide 20
Sender reaction
When a TCP sender receives an ELFN,
It disables its retransmission timers and enters a “standby” mode
While on standby,
A packet is sent at periodic intervals to probe the network to see if a route has been established
If an acknowledgment is received,
Then it leaves standby mode

## Slide 21: TCP OVER AD HOC WIRELESS NETWORK: ….cntd
Feedback-based TCP (TCP Feedback – TCP-F)
Requires the support of a reliable link layer and a routing protocol that can provide feedback to the TCP sender about the path breaks.
The routing protocol is expected to repair the broken path within a reasonable time period.

## Slide 23: Contd..
Advantages:
Simple, permits the TCP congestion control mechanism to respond to congestion
Disadvantages:
If a route to the sender is not available at the failure point (FP), then additional control packets may need to be generated for routing the route failure notification (RFN) packet.
Requires modification to the existing TCP.
The congestion window after a new route is obtained may not reflect the achievable transmission rate acceptable to the network and the TCP-F receiver.

## Slide 24: TCP OVER AD HOC WIRELESS NETWORK:….cntd
TCP with Buffering capability and Sequence Information(TCP-BuS)
Use feedback information from an intermediate node on detection of a path break.
Use localized query (LQ) and REPLY to find a partial path
Upon detection of a path break, an upstream intermediate node originates an explicit route disconnection notification (ERDN) message.
Advantages
Performance improvement and avoidance of fast retransmission
Use on-demand routing protocol
Disadvantages
Increased dependency on the routing protocol and the buffering at the intermediate nodes
The failure of intermediate nodes may lead to loss of packets.
The dependency of TCP-BuS on the routing protocol many degrade its performance.

## Slide 26
Ad Hoc TCP (ATCP)
uses a network layer feedback mechanism to make the TCP sender aware of the status of the network path
Based on the feedback information received from the intermediate nodes, the TCP sender changes its state to the persist state, congestion control state, or the retransmit state.
When an intermediate node finds that the network is partitioned, then the TCP sender state is changed to the persist state.
The ATCP layer makes use of the explicit congestion notification (ECN) for maintenance for the states.

## Slide 28: OTHER TRANSPORT LAYER PROTOCOLS: ….cntd
Application Controlled Transport Protocol (ACTP)
A light-weight transport layer protocol and not an extension to TCP.
ACTP assigns the responsibility of ensuring reliability to the application layer.
It is more like UDP with feedback of delivery and state maintenance
ACTP stands in between TCP and UDP where TCP experiences low performance with high reliability and UDP provides better performance with high packet loss in ad hoc wireless networks.

## Slide 29
Application Controlled Transport Protocol The key design philosophy of ACTP is to leave the provisioning of reliability to the application layer and provide a simple feedback information about the delivery status of packets to the application layer.
ACTP supports the priority of packets to be delivered, but it is the responsibility of the lower layers to actually provide a differentiated service based on this priority

## Slide 30
Application Controlled Transport Protocol Each API function call to send a packet [SendTo()] contains the additional information required for ACTP such as the maximum delay the packet can tolerate (delay), the message number of the packet, and the priority of the packet.
The message number is assigned by the application layer, and it need not to be in sequence. The priority level is assigned for every packet by the application.
It can be varied across packets in the same flow with increasing numbers referring to higher priority packets.
The non-zero value in the message number field implicitly conveys that the application layer expects a delivery status information about the packet to be sent

## Slide 31
Application Controlled Transport Protocol This delivery status is maintained at the ACTP layer, and is available to the application layer for verification through another API function IsACKed<message number>.
The delivery status returned by IsACKed<message number> function call can reflect (i) a successful delivery of the packet (ACK received), (b) a possible loss of the packet (no ACK received and the deadline has expired), (iii) remaining time for the packet (no ACK received but the deadline has not expired), and (iv) no state information exists at the ACTP layer regarding the message under consideration.
A zero in the delay field refers to the highest priority packet, which requires immediate transmission with minimum possible delay. Any other value in the delay field refers to the delay that the message can experience

## Slide 32
Advantages
Provides the freedom of choosing the required reliability level to the application layer.
Scalable for large networks
There is no congestion window
Maintain the end-to-end semantics of TCP
Compatible with traditional TCP
Provides a feasible and efficient solution to improve throughput of TCP
Disadvantages
It is not compatible with TCP.
Could lead to heavy congestion
The dependency on the network layer protocol to detect the route changes and partitions
The addition of a thin ATCP layer to the TCP/IP protocol changes the interface functions currently being used.

## Slide 33: OTHER TRANSPORT LAYER PROTOCOLS: ….cntd
Ad hoc Transport Protocol (ATP)specifically designed for ad hoc wireless networks and is not a variant of TCP and differ from TCP in the following ways:
Coordination among multiple layers
Rate based transmissions
Decoupling congestion control and reliability
Assisted congestion control
ATP uses information from lower layers for
Estimation of the initial transmission rate
Detection, avoidance, and control of congestion
Detection of path breaks

## Slide 34
Ad Hoc Transport Protocol Unlike TCP, ATP utilizes a timer-based transmission, where the transmission rate is decided by the granularity of the timer which is dependent on the congestion in the network.
The congestion control mechanism is decoupled from the reliability and flow control mechanisms.
The network congestion information is obtained from the intermediate nodes, whereas the flow control and reliability information are obtained from the ATP receiver.
The intermediate nodes attach the congestion information to every ATP packet and the ATP receiver collates it before including it in the next ACK packet.

## Slide 35
Ad Hoc Transport Protocol Intermediate nodes attach the current delay information to every ATP data packet if the already existing value is smaller than the current delay.
The ATP receiver collects this delay information and the weighted average value is attached in the periodic ACK (ATP uses SACK mechanism, hence ACK refers to SACK) packet sent back to the ATP sender.
During a connection startup process or when ATP recovers from a path break, the transmission rate to be used is determined by a process called quick start.
During the quick start process, the ATP sender propagates a probe packet to which the intermediate nodes attach the transmission rate (in the form of current delay), which is received by the ATP receiver, and an ACK is sent back to the ATP sender

## Slide 36
Ad Hoc Transport Protocol The ATP sender starts using the newly obtained transmission rate by setting the data transmission timers.
During a connection startup, the connection request and the ACK packets are used as probe packets in order to reduce control overhead.
The receiver performs a weighted average of the delay/transmission rate information for every incoming packet to obtain the transmission rate for an ATP flow and this value is included in the subsequent SACK packet it sends

## Slide 37
Ad Hoc Transport Protocol ATP has three phases, namely, increase, decrease, and maintain The current transmission rate is updated to the new transmission rate if the new transmission rate is lower than the current transmission rate.
In the maintain phase, if the new transmission rate is higher than the current transmission rate, but less than the above mentioned threshold, then the current transmission rate is maintained without any change

## Slide 38
Ad Hoc Transport Protocol If an ATP sender has not received any ACK packets for two consecutive feedback periods, it undergoes a multiplicative decrease of the transmission rate.
When a path break occurs, the network layer detects it and originates an ELFN packet toward the ATP sender. The ATP sender freezes the sender state and goes to the connection initiation phase.
In this phase also, the ATP sender periodically originates probe packets to know the status of the path. With a successful probe, the sender begins data transmission again.

## Slide 39
Advantages:
improved performance, decoupling of the congestion control and reliability mechanisms, and avoidance of congestion window fluctuations
Disadvantages:
The lack of interoperability with TCP
Fine-grained per-flow timer may cause the scalable problem